## Slide 1: EE_735 Assignment_3
3/09/2017

## Slide 2: Numerical solution of PN junction diode
Parameter values are same as given in assignment problem.
Lets denote total device length by L cm.
Lets divide L into N nodes. Let h be the spacing between two consecutive nodes. h=L/(N). (h=L/(N-1)) will also do.
Our aim is to solve : ΔV = - J\F . These terms have been described in the additional material.
Lets try to derive matrix representation of J and F.
Note: The simulation results are shown for abrupt junction case only.

## Slide 3: Terms and their meaning
V - potential profile; Vt = kT/q is the thermal voltage; n – electron concentration; p - hole concentration; ni - intrinsic carrier concentration; Nd -donor dopant concentration; Na - acceptor dopant concentration; Ndop – net doping profile; φn = Vt * log(Nd/ni); φp = Vt * log(Na/ni); ε = 12 * ε0 (where ε0 is the permittivity of vacuum).
V
φn
V
-φp
node N
Nodes
node1
N side
P side
φn
-φp
node N
node N/2
V(N/2)
V((N/2)+1)
Nodes
Some V profiles which can be used as an initial guess
node1
V=0
V=0

## Slide 4: Doping profile
Ndop(1)
Ndop(2)
Ndop(N)
.
.
.
Ndop =
Ndop
Nd
Ndop
-Na
node N
Nodes
node1
N side
P side
Nd
-Na
node N
node N/2
Ndop(N/2)
Ndop((N/2)+1)
Nodes
node1
Ndop=0
Ndop=0
Nx1
Abrupt junction
Linearly graded junction

## Slide 5: V, n and p
V =
V (1)
V (2)
V (N)
.
.
.
Nx1
n =
ni*exp(V (1)/Vt)
ni*exp(V (2)/Vt)
ni*exp(V (N)/Vt)
.
.
.
Nx1
p =
Nx1
ni*exp(-V (1)/Vt)
ni*exp(-V (2)/Vt)
ni*exp(-V (N)/Vt)
.
.
.

## Slide 6: b matrix
Ndop(1)+p(1)-n(1)
Ndop(2)+p(2)-n(2)
Ndop(N/2)+p(N/2)-n(N/2)
Ndop((N/2)+1)+p((N/2)+1)-n((N/2)+1)
Ndop(N)+p(N)-n(N)
Ndop(N-1)+p(N-1)-n(N-1)
ρ = q *
.
.
Nx1
.
.
p(1)/(-Vt)-n(1)/Vt
p(2)/(-Vt)-n(2)/(Vt)
p(N/2)/(-Vt)-n(N/2)/Vt
p((N/2)+1)/(-Vt)-n((N/2)+1)/Vt
p(N)/(-Vt)-n(N)/Vt
p(N-1)/(-Vt)-n(N-1)/Vt
; Δρ = q *
.
.
Nx1
.
.
b = -(ρ/ε) ; Δb=-(Δρ/ε)

## Slide 7: F matrix and boundary conditions
V(1)- b(1)
(V(1)-2*(V(2))+V(3))/h2- b(2)
(V(N-2)-2*(V(N-1))+V(N))/h2- b(N-1)
V(N) - b(N)
(V(2)-2*(V(3))+V(4))/h2- b(3)
(V(N-3)-2*(V(N-2))+V(N-1))/h2- b(N-2)
.
.
.
F=
Nx1
b(1) = V(1) and b(N) = V(N) ;
where V(1) and V(N) are fixed potentials.
Δb(1) = 0 and Δb(N) = 0;
These are the Boundary conditions and shouldn’t change during subsequent iterations.

## Slide 8: Jacobian matrix (J)
1-Δb(1)
1-Δb(N)
-2/h2 -Δb(2)
1/h2
1/h2
Columns
rows
0
. . .
0
1
2
3
N
4
-2/h2 -Δb(N-1)
1/h2
1/h2
N-1
0
1
2
N-1
N
0
. . .
0
N-2
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
. . .
-2/h2 -Δb(3)
1/h2
1/h2
0
. . .
0
0
0
-2/h2 -Δb(N-2)
1/h2
1/h2
0
0
0
. . .
0
.
.
.
N-2
NxN

## Slide 9: Simulation results
There is a problem at the boundaries. We have used p=ni * exp(-V/Vt). We have fixed V(1)=0, which yields p(1)=ni. However p(1) = Na, since it belongs to the bulk. Thus this boundary condition is not satisfying hole concentration in the bulk. Similar reasoning can be given for n. (Note : x < 0 is P type and x > 0 is N type). It took around 40 iterations to converge. h=L/N has been used.

## Slide 10: Simulation results
This graph is similar to the previous one. Here we have reduced the step size ‘h’ by increasing the number of node points ‘N’. Thus varying h within the range 1e-8 cm to 1e-6 cm did not result in convergence issues. h=L/N has been used.

## Slide 11: Simulation results
We have fixed V(1)=-φp and V(N)=φn, which yield correct values for n and p at the boundaries. It took around 50 iterations to converge. h=L/N has been used.

## Slide 12: Simulation results
This graph is same as the previous one. h=L/(N-1) has been used.