EE 735: ASSIGNMENT 4 REPORT
NAME: DIMPLE KOCHAR
ROLL NO.: 16D070010

Note: Analytical solutions of all problems are at end. All concentrations (meaning density) are in cm-3 and x is in cm in plots.

Q1 a)

Comparing these two plots by plotting them together, we see that they superimpose each other

flux at A = -1.72709*1016
flux at B = -1.07696*1014
flux from A to B =
flux at B – flux at A =
1.71632*1016

Q1 b)

Comparing these two plots by plotting them together, we see that they superimpose each other

flux at A = -1.7270*1016
flux at B = -5.8944*1012
flux from A to B =
flux at B – flux at A =
1.72643*1016

Using this boundary results in nearly same flux at A and same flux from A to B. However, flux at B changes due to this boundary condition as outgoing flux becomes a function of density at B.

Q1 c)

Comparing these two plots by plotting them together, we see that they superimpose each other

flux at A = 1.7736*1011
flux at B =-1.7067*1010

Q2
We take N = 1001 gridpoints from x = 0 to 10-3 cm. So, h = 10-6 cm
This gives us p = 5*10-9 sec
Running for 1000 such time steps, means we run till = 5*10-6 sec

All 1001 graphs:	Zoomed plot:

1st 10 plots:	plots after 0.25us intervals (21 plots)
Comparison with analytical:

I don’t get exactly matched numbers, but their order is same as that of analytical.

As we see in our analytical solution, we have a gaussian profile with sigma2 = 2*D*t, i.e. profile has a variance which is time dependent. As time passes and variance increases, we see the graph has flattened more which is expected due to diffusion. Increasing D too results in faster flattening as compared to this graph.

Q3.

We take N = 101 gridpoints from x = 0 to 10-2 cm. So, h = 10-4 cm
This gives us p = 1.6667*10-10 sec
Running for 1000 such time steps, means we run till = 1.6667*10-7 sec

Plotting all 1001 plots and comparing with analytical:(1st plot all 0-inital)

plots after 2.5ms intervals (21 plots) (1st plot all 0-inital)

1st 10 plots:

Q4.
Ea = 3.69 eV, D0 = 10.5 cm2/sec
Keeping neumann boundary conditions at right boundary and keeping left boundary at n=0 (using neumann boundary at left boundary also doesn’t change thermal budget

Thermal Budget = 1.36408*10-11 cm2

At 1000 degrees celsius, when slope roll off is 40nm/decade at junction depth:

(slight error in answer due to numerical inaccuracies)

time (sec)	D (cm2/sec)	Temperacture (celsius)
512.0253	2.6641*10-14	1000
1.4132*1012	9.6526*10-24	500
0.0392	3.4804*10-10	1500